## Slide 1: Beam_analysis – data processing
X
Y
Z

## Slide 2
Input (provided): four db tables:
  ba_g,
  ba_mat,
  ba_loading,
  ba_spt
  el_max: maximum element length
Get all rows for each db table using given value for field “userscalcPK” = 104 (i.e.),
Save all retrieved data to an array $data with “geometry”, “material”, support”, and “loading”.

## Slide 3
Output:
  array $nodes having fields: id, x, y, z.
    id: the Node ID;
    x/y/z, the x/y/z coordinates of an node. y/z=0 in this case.
    Needs to log nodes from the given db tables and generate nodes by dividing sections defined between two nodes.
  array $ele having fields: id, node_s, node_e, PK4ba_mat, PK4ba_g
    Id: the element id – one element connecting two nodes;
    Node_s, Node ID of the starting node of the element;
    Node_e: Node ID of the ending node of the element;
    PK4ba_mat : the value of the field matID in ba_g which is the primary key value of ba_mat;
    PK4ba_g: the value of the field rcdNo in ba_g

## Slide 4
Output:
  array $loading having fields: id, fx, fy, fz, mx, my, mz
    id: the node ID;
    fx / fy: 0
    fz:
      Case “geometry” = “Point” and “type” = “Force”, fz = startValue for id (node ID) whose x = startLocation;
      Case “geometry” = “Distributed” and “type” = “Force”, fz = see LAST pages
    mx / mz: 0
    my:
      Case “geometry” = “Point” and “type” = “Moment”, my = startValue for id (node ID) whose x = startLocation;
      Case “geometry” = “Distributed” and “type” = “Moment”, my = see last pages.
      Mx / mz: 0

## Slide 5
ba_mat

## Slide 6
ba_g
ba_spt

## Slide 7
Every “start” and “end” should be a node;
- db table: ba_g
Every support “location” should be a node;
- db ba_spt
X
Y
Z

## Slide 8
ba_loading

## Slide 9
X
Y
Z
Between given/known locations (HARD NODE locations) where a node is a must, equally divide sections between HARD NODES into many small sections so that the length of each section is less or equal to given “el_max” . If the length between HARD NODES is less than “el_max” , then no need to divide.
The Start/End Locations of loading with Geometry = Distributed, Type = Force / Moment are HARD NODES as well.

## Slide 10
Distributed Force
Distributed Moment
X
Y
Z

## Slide 11
HARD NODES
HARD NODES are nodes at locations along the beam where they are:
Start and End of a beam section;
Start or End of a distributed loading;
  Location with value = zero of a distributed loading;
Supports
loading point of point forces/moments
The coordinates of most HARD NODES (except the cross NODE of distributed loading with opposite values at two ends) are given in the provided db tables.

## Slide 12
Equally divide into sections so that the length of sections is less than or equal to “el_max”
For Distributed Force, if the start and end values are of different sign, there will be a ZERO node – need to find that node’s location
a
b
x1
x2
x3
v1
v2
l_sec = X3 – x2 = x2 – x1 <= el_max
v1 = b + (a-b)/x3*x1
v2 = b + (a-b)/x3*x2
Ma = (a - (a-b)/x3 * l_sec/4)* l_sec/2
M2 = v2*l_sec
M1 = (v1 + (a-b)/x3 * l_sec/4)* l_sec/2
+ (v1 - (a-b)/x3 * l_sec/4)* x1/2
Mb = (b + (a-b)/x3 * x1/4)* x1/2
Ma + M2 + M1 + Mb = (a + b)*x3
X3/N = l_sec <= el_max
Need to consider the case having a Point Force/Moment OR support located within Distributed Force/Moment
$loading

## Slide 13
HARD NODES
Equally divide each section between two neighboring HARD NODES into multiple sections so that the length of sub-sections between all neighboring HARD NODES is less than or equal to given “el_max”
If the distance between two neighboring HARD NODES is less than “el_max”, no division is needed.
Sections between neighboring HARD NODES

## Slide 14
Suggested logic steps:
Find all HARD NODES and create elements connecting neighboring nodes
  Beside all HARD NODES given in the db tables, need to loop through all distributed loading: Distributed Force/Moment by checking if it has opposite signs at start and end.
Loop through all elements, determine the length of each element,
  If the length > el_max, equally divide the element into several sections until the length of each section is <= el_max
  Logging the support on nodes
  Logging the point load on nodes
  Loop through all Distributed Force/Moment
    Find the nodes for the start and end locations of the Distributed Force/Moment
    Determine the FZ - foce (MY - moment) of all nodes from start to end.