## Slide 1: Spec
2016-02-23

## Slide 2
See db_changes.xlsx db table changes.
Move all db query to Database.class.php:
Placing “$query = "SELECT `E` FROM `ba_mat` WHERE `rcdNo`=";” in public function generateKE_1() in FEA.class.php is not good
In addition to pre.php and post.php, prepare call2analysis.php file so that other code can call this file to run the analysis and generate all json files (following slides for more details). No need to print out any variables on the page when calling call2analysis.php

## Slide 3
Two db tables added: ba_nodes, ba_lcs where ba_nodes records the coordinates of a set of nodes; ba_lcs records the combinations of ilcs saved in ba_ilcs by assigning each ilcs a coefficient in the lcs.
DB tables renamed:
  ba_g  ba_sections
  ba_loading  ba_ilcs
  ba_mat  ba_materials
  ba_spt  ba_supports

## Slide 4
According to the given node number [n_start] and [n_end] in table “ba_sections”, retrieve the corresponding coordinate values from table “ba_nodes” (currently, the coordinate values are given in [start] and [end] in “ba_g”).

## Slide 5
To retrieve the data from db table “ba_units”
For all numeric data/value retrieved from tables “ba_X”, performing a unit conversion with the “unitConversion” function in unitConversion.php:
$value2be = unitConversion($crtValue, $crtUnit, $unit2be) where $unit2be are “ft, lbf, …”

## Slide 6
Use the E, I, A, le, etc after unitConversion to calcualte EI, etc in k_e’s calculation.
Perform the “runAnalysis” for each ilc and lc (lc is a combination of multiple ilcs with a coefficient for each ilc). Save the results for al ilcs and lcs to json file.

## Slide 7
The mesh is still the same – using all ilc and others to determine hard nodes, etc.
Save nodes, elements, and loading (all ilcs and lcs) information after mesh to json file:
  Nodes: id, x, y, z
  Elements, id, n_start, n_end, E, Rho, G, A, Ix, Iy
  ilc: node_id, fx, fy, fz, mx, my, mz (do not list of all values are zero)
  lc: the result of c1*ilc1 + c2*ilc2 + …
  These data can be in one jason file: model.json

## Slide 8
Save the result for all ilcs and lcs to a json file result.json. For each ilc/lc, the file include:
Node_id, dx, dy, dz, rx, ry, rz, qx, qy, qz, mx, my, mz
When giving ilc or lc, the corresponding data for that ilc or lc in the json file should be able to be retrieved and returned to a variable.